## Slide 1: OMA-ARC-2012-0140-INP_Notification_Channel_NetAPI_Enabling_OMA_Push_Delivery_Method Notification Channel Enabling OMA Push Delivery Method
Submitted To: ARC
Date: 29 June 2012
Availability: Public OMA Confidential
Contact: Shahram Mohajeri, sm7084@att.com
Source: AT&T
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2
Page 2
API Server
Notification Server
1- POST: Create Notif. Channel (Ch-Type =Long Polling,…)
Enabler X
Enabler X
2- CallBack URL, Channel URL
Existing Server to Mobile Notification using Long Polling Delivery Method through Notification Channel API
4- Subscribe to Notification +Callback-URL
5 Internal Notifications sent to
Callback-URL@ Notification Channel
6- POST: Long-Polling on Channel URL
3- RESTful API Subscribe to Notification (…, NotifyURL= Callback-URL)
Example: Payment API: POST /exampleAPI/payment/v1/tel%3A%2B19585550100/transactions/amount(…, NotifyURL= Callback-URL)
7- Notifications as in reply to POST
App client in the absence of an APP-Server, first asks the Operator’s Notification Channel Server (Notification Server for short) for a Callback URL and a Long-polling channel URL.
Notification mechanism between API Server, Notification Server and the Enablers are considered internal matters.
Notification Channel functionality may be implemented as a separate system however, all notifications are monitored by the API Server
Notes: 2

## Slide 3
Page 3
API Server
Notification Server
(PI)
1- POST: Create Notification Channel (Ch-Type =OMA Push, AppId,…)
Enabler X
Enabler X
2- CallBack URL
Server to Mobile Notification using OMA Push Delivery Method through Notification Channel API
PPG
6- Push (POST:
X-Wap-Applicatin-Id = AppId,…)
7- OMA Push/SMS
“Channel Type” flag would indicate whether Notification Server is to use Long-Polling or OMA-Push delivery method
Channel Type = “OMAPush” tells Notification Server to behave as a Push Initiator (PI)
App would optionally provide the AppId (in step #1) where OMAPush would need to be sent. Note: AppId may or may not be available as part of App on-boarding onto API Server.
Notification Server provides the App only a Callback URL.
Notification mechanism between API Server, Notification Server and the Enablers are considered internal matters. However, all notifications are monitored by the API Server
4- Subscribe to Notification +Callback-URL
5 Internal Notifications sent to
Callback-URL@ Notification Channel
3- RESTful API Subscribe to Notification (…, NotifyURL= Callback-URL)
Example: Payment API: POST /exampleAPI/payment/v1/tel%3A%2B19585550100/transactions/amount(…, NotifyURL= Callback-URL)
Notes: 3

## Slide 4
In C2DM (Android Cloud to Device Messaging) case, the Android App requires to have an App Server. Therefore, OMA Notification Channel is not used
The Notification would follow a Server-Server notification model where operator’s API Server sends network-initiated notification to the App Server
The App Server then interacts with Android C2DM Server in order to push the notifications to the App client on the Android device
Android C2DM service requires the App to have an App-server
  Bypassing 3rd-party App server and having Operator’s Notification Server interacting with C2DM server directly does not make sense as C2DM server requires on-boarding of the 3rd-party App server as part of the application registration which also entails application’s OAuth redirect-URI registration and management of the App’s Registration Id, etc
  Notification Channel Server-to-C2DM direct interaction would mean tight integration of Notification Server with C2DM server which would introduce other unnecessary complexities (i.e. Notification server would need to behave like the App Server towards C2DM; e.g. manage App’s Registration Id, and OAuth tokens generated by C2DM). Whereas all such complexities should be handled by the developer’s App server, if he/she chooses to use Android C2DM delivery method instead of OMA push
Server–Server Notification With App Server using C2DM Delivery Method

## Slide 5
Page 5
Server–Server Notification With App Server using C2DM Delivery Method
App
Server
API Server
Enabler X
Enabler X
5-RESTful API Notifications
sent to callback URL
2-Record Callback URL
API Server is the platform via which all the notifications are proxied as both OMA RESTful API protocol adaptation as well as notification validity based on client App’s OAuth token would need to be performed before notification is directed to the App Server
Notification mechanism between App Server and App client through C2DM server is out of scope (i.e. step #6 & #7)
Android
C2DM
Server
6- Post https://android.apis.google.com/c2dm/send
7- Push using “Android Intents”
3- Subscribe to Notification
4-Internal Notifications received
1- RESTful API (…, NotifyURL= Callback-URL@AppServer)
Notes: 5

## Slide 6
In APNS (Apple Push Notification Service) case, the iOS App requires to have an App Server. Therefore, OMA Notification Channel is not used
The Notification would follow a Server-Server notification model where operator’s API Server sends network-initiated notification to the App Server
The App Server then interacts with iOS APNS Server in order to push the notifications to the App client on the iOS device
Apple APNS service requires the App to have an App-server
  Bypassing 3rd-party App server and having Operator’s Notification Server interacting with APNS server directly does not make sense as APNS server requires on-boarding of the 3rd-party App server as part of the application registration which also entails application’s SSL certificate and Private key and iOS device token management
  Notification Channel Server-to-APNS direct interaction would mean tight integration of Notification Server with APNS server which would introduce other unnecessary complexities (i.e. Notification server would need to behave like the App Server towards APNS; e.g manage App’s SSL certificate, private key, iOS device token etc). Whereas all such App-specific complexities should be handled by the developer’s App server.
Server–Server Notification With App Server using APNS Delivery Method

## Slide 7
Page 7
Server–Server Notification With App Server using APNS Delivery Method
App
Server
API Server
1- RESTful API (…, NotifyURL= Callback-URL@AppServer)
Enabler X
Enabler X
2-Record Callback URL
API Server is the platform via which all the notifications are proxied as both OMA RESTful API protocol adaptation as well as notification validity based on client App’s OAuth token would need to be performed before notification is directed to the App Server
Notification mechanism between App Server and App client through APNS server is out of scope (i.e. step #6 & #7)
Apple
APNS
Server
6- Push message
7- Push message
3- Subscribe to Notification
4-Internal Notifications received
5-RESTful API Notifications
sent to callback URL
Notes: 7

## Slide 8: Recommendation
Enhance OMA Notification Channel API to support notification delivery via OMA Push
  “OMAPush” an additional value in “ChannelType” enumeration
  ChannelType = “OMAPush” would mean new delivery behaviour by Notification Channel Server
  AppId, an optional parameter in the Notification Channel creation operation
Usage of Google Android C2DM or Apple APNS schemes by the 3rd-party Apps does not require OMA Notification Channel involvement
  To accommodate the use of existing C2DM or APNS schemes, an App on the mobile device that uses OMA RESTful APIs would need to use the typical subscription mechanism available as part of the OMA RESTful API by passing a callback URL. The API Server will then POST notifications to that URL.
ARC group is kindly requested to discuss and determine if CR process can be used to expedite enhancement to Notification Channel API V1.0 in support of the OMA Push delivery method