## Slide 1: OMA-ARC-2014-0050-INP_revised_draft_WID_to_implement_SmaC_RD Draft WID to implement SmaC
Submitted To: ARC
Date: May 23 2014
Availability: Public OMA Confidential
Contact: Eldad Zeira, InterDigital,
eldad.zeira@interdigital.com
Source: InterDigital
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Summary
In [1] OMA has defined a set of requirements for use cases enabled by small cells capabilities.
In the context of the cooperation agreement between OMA and SCF the latter has recently requested [2] OMA to commence generation of normative specifications to address the requirements agreed on presently.
Gap analysis shows that existing APIs do not meet the spirit and letter of [1]. Alternatives to [1] have also been examined and fall short of perceived needs.
SCF has already performed work we could use as a basis [7]
The attached (draft) WID aims to start the discussion to lead to OMA undertaking of that task.

## Slide 3: The Small Cell Context
Small Cells are low-power wireless access points that enable Mobile Operators and Service Providers to increase their networks’ capacity and quality in a sustainable way.
Clusters of small cells may be formed based on location and / or other parameters (e.g. ownership)
Clusters can also be treated as zones though zones may include macro cells
Cell Cluster offer peculiar capabilities that can be exposed, through convenient APIs, to Application Developers, in order to enhance Apps with new functionalities.

## Slide 4: Zones
Zones may be formed as clusters of small and other cells, aka Access Points
AP in zone need not be contiguous (forming “islands”)
The footprint of each “island” can vary
An AP may belong to multiple zones at the same time
Examples of zones:
  All “Starbucks” cafes in Manhattan
  All “Home Depot” stores in NYC
  The Roosevelt Field Mall
  Places that parents with children frequent on Sundays
  Cars of commuter trains (equipped with a wifi connection)

## Slide 5: Previous OMA APIs
Are similar with respect to location
Terminal location API [6]
  Obtain the current terminal location
  Obtain the terminal distance from a given location
  Obtain the distance between two terminals
  Manage subscriptions
Presence API [5]
  Watcher retrieves presence information for a single Presentity
  • Watcher retrieves presence information for Presentities in a Presence List
  Returns:
  PlaceType value (RFC4480)
  Location value (lat/lon or address) - (RFC5491, 4119 & 5139)

## Slide 6: Zonal Presence vs. Presence API
Zonal Presence (SmaC RD)
Based on attachment point in zone:
  Is the user in the zone?
  At which AP in the zone is the user?
  List / locations of AP in zone
  List / count of users in zone or at AP
Assumes interface to small cell entity which:
  knows zone context
  Always aware of location of UE relative to zone
Existing NetAPIs
Based on geo-location
  Where in the world is the user?
  Location specified in Lat/Lon, address and type of location
Assumes interface to an entity which is not aware of zones

## Slide 7: RD - NetAPI Gap analysis
Label | Description | Met with NetAPI?
SmaC-ZP-001 | Expose to authorized applications the following: Initiate and terminate subscription to Zonal Presence notifications Query list of zones, zone status, status for access points within a zone Query users Zone as a collection of access points that may be in one or more sites, and where each site may have one or more access point. Each zone will have a unique "Zone ID" identifier. | NO Zone not defined; Even if AP are known to MN, their status within a zone isn’t as zone is unknown No ability to query for users in zone
SmaC-ZP-002 | Desirable to be RESTful | Yes
SmaC-ZP-003 | The mobile identity of the device shall be common with that consumed by other OneAPI API's. | Yes
SmaC-ZP-004 | The Initiate Subscription to Zonal Presence Notifications operation shall include Zone ID & Notification URL - the location where notifications are sent | NO Zone and Zone ID not defined
SmaC-ZP-005 | A response to the Initiate Subscription to Zonal Presence Notifications operation shall confirm the subscription. | Yes
SmaC-ZP-006 | A Zonal Presence Notification shall include one or more events of the following type: Zone Enter - A mobile device entered a zone by camping on to one of its access points. Zone Exit - A mobile device handed over to an access point out of a zone from one that was inside the zone. Zone Transfer - A mobile device moved between access points within a zone. | Marginal – geo location can be provided but is difficult to relate to APs in area

## Slide 8: RD - NetAPI Gap analysis, cont’d
SmaC-ZP-007 | The Query List of Zones operation shall return a list of zone ID's visible to the authorized user. | NO No concept of Zone ID
SmaC-ZP-008 | As a function of a Zone ID, the Query Zone Status operation shall provide a response containing: The Zone ID Number of users currently in the zone Number of access points in the zone Number of unserviceable access points. | NO No knowledge of APs as a part of a zone
SmaC-ZP-009 | The Query Status for Access Points Within a Zone operation shall provide a means to query the status for all access points as a function of a Zone ID, or a named set of access points for a given Zone ID. Each access point in the result shall contain the following parameters: Location and altitude Access point type that indicates either femto, LTE-femto, WiFi or Wimax type Operational status indicating either serviceable or unserviceable condition Number of mobile devices camped on the access point | No No support for AP geo-location
SmaC-ZP-010 | The Query Users operation shall return a list of mobile devices camped onto the access point(s) within a zone. For each user, it shall return the following parameters: Mobile identity Access point ID It shall be possible to query for a specific user, list of users on a given access point or all users within a zone. | No AP ID cannot be provided

## Slide 9: Relevant SCF work
SCF has published a Zonal Presence API (RESTful) which provides [7]:
  Initiate subscription to zonal presence notifications
  Cancel subscription to zonal presence notifications
  Zonal presence notification
  Query zone list
  Query zone status
  Query a named set of access point status
  Query all access point status
  Query a user within a zone
  Query all users on an access point
  Query all users within a zone
This API may be used as a basis for OMA work, if desired
  (though it should be checked / modified to comply with OMA guidelines)

## Slide 10: Summary
Existing NetAPI do not allow operators to provide presence information in the context of a zone
OMA has previously recognized that fact and has approved, but not implemented, an RD
Small Cell Forum has formally requested OMA to implement its RD
An implementation already exists and can be used as a basis for our work

## Slide 11: OMA-WID_pqrs-SMAC_API_implementation-V1_0-2014xxxx-D Work Item Document Wpqrs – SMAC_API_Implementation_ V1.0
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.
Date: xx May 2014
Availability: Public OMA Confidential
Contact: Eldad Zeira, eldad.zeira@interdigital.com
Source: InterDigital
X
DRAFT
Notes: This is the new Work Item Definition (WID) template. It is in PowerPoint format so that it also serves to present the Work Item to TP and assist in its socialization. Keep in mind that this is a permanent document, so it is important to provide information that is as detailed and exact as possible.

## Slide 12: Work Item Title and Registration Name
Work Item Title | Working Group | Registration Name | Version number
Small cell cluster API | OMA ARC | SmaCAPI | 1.0
Enabler type: ??
Notes: The Work Item Title is the formal name of the WI. The Work Item Title SHOULD be chosen so that readers can quickly grasp the general idea of the WID and easily associate it with the corresponding WID name. The Work Item Title and Registration Name SHALL NOT include version numbers. Abbreviations SHOULD be avoided. The Version refers to the version of the Enabler Release or Reference Release to be specified by the Work Item.
An example of correct WI naming:
Work Item Title Working Group Registration Name Version Name
Device Management DM DM 3.0
An example of incorrect WI naming:
Work Item Title Working Group Registration Name Version Name
Device Management 3.0 DM DM 3.0

## Slide 13: Description and Objectives
Work Areas: Small cell based API for value added services
Issues this Work Item aims to solve:
  zonal presence 1 in a small cell group
Market benefits: Enable service (application) providers to take advantage of the small cell as a service delivery platform
Time to market: 1 year
Expected market acceptance: high (based on SCF interest and formal request)
Complexity:
  Low for implementing existing RD for UMTS
  EPC authorization requirements could be more complex
Uniqueness: while the technology to provide location and other services does exist, the new API will provide these services in the context of a cluster of small cells
1 Clause 6.1.2 in the RD [1]
Notes: The completion of a Work Item (WI) takes time, effort and enthusiasm. The process of persuading others to join in a WI and to finally complete the task is a major investment for all concerned. It is therefore of paramount importance that the return from such a WI justifies the investment undertaken.
In order to ensure that Business Focus is applied in creating a WI, it is recommended to address the points in this slide. You can use several slides to address these points if necessary:
Work Areas should provide a sufficiently good understanding of the technical results to be delivered by the WI, but they should not define how the required functionality is to be specified or how it is to be implemented.
Issues this Work Item aims to solve addresses the problem experienced by the market players and end users (i.e. the value chain) to be solved by this WI. This point should provide assurance that the WI is not trying to provide a solution for which there is not a clear problem in the market.
Market benefits describes the benefits this WI will bring to the value chain (e.g. the subscriber, the operator etc.) in the market
Time to market should address impacts from doing the work as well as from not doing the work.
Expected market acceptance should justify how and why the market will accept this solution.
Complexity should describe how this WI increases or decreases complexity in terms of user experience, configuration, operations and component deployment (including costs of new equipment). Indicate whether there are any issues that affect the ability to operate in an all-IP environment, for example the need to use SMS or to assign telephone numbers to devices etc.
Uniqueness should address the uniqueness of the work covered by this WI. Describe any cases where similar work is underway or being proposed within OMA or outside OMA.

## Slide 14: Main Use Case(s) – 1’st phase
The owners of a store chain want to provide their customers with real time information regarding merchandise availability and prices. The owners are notified when a participating customer is at any of their stores, regardless of the physical location of these stores.
Owner may request and receive:
  List of AP in stores and their locations
  List / count of users in any of their stores
A metropolitan transportation agency tracks commuters habits and defines high traffic zones.
  The agency then receives real time information on commuters count in each AP in these zones
Notes: Very often a WID refers to one or a few very significant use case(s) to explain the purpose of the proposed work.
Use one or more slide(s) to explain the main use case(s) included in the WID.
The use of drawings and animations is much encouraged.

## Slide 15: Impacts, Relationships and Dependencies
Existing specifications affected: none
Other Work Items affected: none
OMA WGs and external organizations affected: TBD
Impacts on Architecture, Charging/Billing, Security, Privacy, IOT: IOT test cases to be developed
Notes: List any specifications, Work Items, Working Groups or external organizations that may be affected by this work or are otherwise related.
Identify any impact on OMA Architecture, Charging and Billing Enablers, Security, Privacy and Interoperability Testing (IOT).

## Slide 16: Proposed Timeline
TBD
Notes: Double click on the embedded Excel sheet and enter the dates for the proposed WI schedule in the table in sheet2. The dates need to be set for UK style YYYY-MM-DD. Filling instructions are in the file.
The Excel file will calculate durations and creates the graph. Copy/paste the table and graph from Excel into slide.
Please note that the 'AD start' date should be aligned with the ‘New reqs deadline’. It is not necessary to provide any milestones beyond Candidate status (e.g. for IOP testing, public review or Approved status).

## Slide 17: Planned deliverables
Requirements
  The current SmaC RD will be revised and prioritized as needed
Architecture
  An architecture document will be developed
Development Phase
  APIs
  IoP plans
Notes: List the planned Deliverables for each of the phases of the Process (Requirements, Architecture and Development). You can choose from the options provided above.
Please note that the OMA Process allows for lightweight development (a.k.a. “fast track development”. This means that a WI can omit Deliverables or combine Deliverables in a Combined Release Document.
Typical examples are combining Architecture and Technical Specifications into a Combined Release Document or combinging Requirements, Architecture and Technical Specifications into a Combined Release Document.
Reference Releases may be made up of any documents including white papers.
Deployment Suites typically only contain Test Specifications.

## Slide 18: Planned reviews
Requirements
  TBD
Architecture
  TBD
Release
  TBD
Notes: List the reviews that are planned for each phase (if any).
Please note that the OMA Process allows for lightweight development (a.k.a. “fast track development”. This means that a WI can omit any formal review or replace it with a closure review or an informal review.
It is strongly recommended to define reviews that are line with the complexity and expected quality of the planned Release. Generally speaking it is always recommended to have a Consistency Review before submission to TP for approval as Candidate.
For definitions of Formal Reviews, Closure Reviews and Consistency Reviews, please see the OMA Organization and Process document.

## Slide 19: Supporting Companies
The companies supporting this work item are:
Company name | Membership type
InterDigital | Full
AT&T | Sponsor
Notes: List all of the supporting companies in order of membership and then in alphabetic order. Example:
Marvellous Mobiles, Sponsor
Serious Servers, Sponsor
Acme Associates, Full
Haptic Handsets, Full
Durable Databases, Associate
Please note that a Work Item must have at least four supporting companies before it can be approved by TP and start work.

## Slide 20: Proposed Resources
The companies supporting this work item are proposing the following resources:
Deliverable/Role | Proposed volunteer editor/champion
Requirements document | Eldad Zeira, InterDigital
WID/WISPR Champion | TBD
ARC document | TBD
Technical Specifications | TBD
Notes: While not mandatory, it is strongly recommended to list as many volunteers and resources as possible.
You can add or remove deliverables and roles in the above table as appropriate.
This initial list does not preclude anyone outside the group of supporting member companies to volunteer for one or more of these roles once the work item has been assigned to a WG and the work has started.

## Slide 21: Document History
Approved Versions
Draft Version 1.0
Version | Date | Notes
X.Y | dd mmm yyyy | 
Date | Changes
Notes: This slide records the change history of the document. Please record each Approved version and its approval date. For each Draft version, indicate the main changes made with each change request.
This slide does not need to be presented to TP.

## Slide 22: References
SmaC RD V1.0 http://member.openmobilealliance.org/ftp/Public_documents/ARCH/Permanent_documents/OMA-RD-SmaC-V1_0-20130121-D.zip
LS from http://member.openmobilealliance.org/ftp/Public_documents/ARCH/2014/OMA-ARC-2014-0033-ILS_from_Small_Cell_Forum_on_Follow_up_Request.zip
http://member.openmobilealliance.org/ftp/Public_documents/ARCH/2014/OMA-ARC-2014-0032-Reply_LS_from_Small_Cell_Forum_on_OMA_LS_997.zip
SCF ARCH http://www.scf.io/en/documents/067_-_Enterprise_small_cell_network_architectures.php
OMA-TS-REST_NetAPI_Presence-V1_0-20130212-C
OMA-TS-REST_NetAPI_TerminalLocation-V1_0-20130924-A
084 Small Cell Zone Services http://scf.io/en/documents/084_-_Small_Cell_Zone_services_RESTful_Bindings.php
Notes: List the reviews that are planned for each phase (if any).
Please note that the OMA Process allows for lightweight development (a.k.a. “fast track development”. This means that a WI can omit any formal review or replace it with a closure review or an informal review.
It is strongly recommended to define reviews that are line with the complexity and expected quality of the planned Release. Generally speaking it is always recommended to have a Consistency Review before submission to TP for approval as Candidate.
For definitions of Formal Reviews, Closure Reviews and Consistency Reviews, please see the OMA Organization and Process document.