## Slide 1: Mobile Network Operator as an Identity Provider –Comparison of Approaches
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.
X
Date: 24 August 2014
Availability: Public OMA Confidential
Contact: Eldad Zeira, eldad.zeira@interdigital.com
Source: InterDigital

## Slide 2: Introduction
Today’s users of applications need to authenticate themselves to multiple application providers, usually using a password. A password alone is a weak authentication technique.
Password (or any other form of credentials) security is greatly enhanced if bound to device authentication
At the Montreal meeting we have introduced the notion of the mobile network operator as an identity provider, building on the credentials in the UICC
To enable this feature,
  The operator will need to activate already available authentication procedures (AKA or, if implemented, GBA)
  OMA will standardize an API to enable the operator to expose his device authentication capabilities to OTT identity providers or application service providers.
At the meeting we have promised to compare our approach to other techniques currently proposed or standardized for user authentication. This is the subject of this paper.
The analysis in this paper represents the author’s best understanding of the various techniques based on publically available material. Your help in verifying my understanding will be highly appreciated.

## Slide 3: Authentication Approaches – High Level Description
Approach | General description
GSMA MobileConnect | User’s PIN is authenticated to modified UICC which has a pre-stored PIN. UICC is authenticated to the operator (not using AKA or operators certificates) which then asserts user’s identity to App service providers. The scheme uses operator identifiers or MS-ISDN as a de-facto identifier for all applications. The scheme does to not seem to be designed for multi-factor authentication and in fact they consider avoiding the need for App passwords a feature.
3GPP SSO | User’s PIN auth. To UICC; GBA used to auth. UICC to NW and provide assertion to App. 3GPP SSO allows either MNO or App provider to become master IDP. 3GPP SSO is based on GBA
FIDO | User is authenticated to smart card. Smart card authenticates to App using Public-Private Key protocol. (MNO will need to support public-private key based authentication)
OpenID Connect (Mobile profile) | Operator sends OTP (one time password) to mobile. User submits it through client and is validated by operator. Operator sends authentication confirmation to service provider.
GBA | AKA credentials used by operator to assert identity to application and bootstrap app keys. Can be done at App request. However password isn’t bound to device. GBA was created for single factor. Adoption of GBA in the 3GPP community is unclear and isn’t normative at this point (33.924).
Proposed | User uses e.g. a password to authenticate to App. App requests MNO to authenticate the user’s subscription via AKA credentials in UICC on same device that was used to submit the password. The user authentication and device authentication are bound to each other.

## Slide 4: Comparison 1/3
Property | GSMA MobileConnect | 3GPP SSO | FIDO | Mobile Profile OpenID Connect | GBA | Proposed
Is an “OpenID”-like scheme required? | Yes | Yes | Not required | Mandatory | Not applicable | Optional / recommended but not required
Multi- factor authentication? | 1 step, 1 factor | Multi- factor | 2 steps, 1 factor per step (relying on the smartcard) | Multi-factor | No | Yes – multi-factors bound either on MNO or service provider side
Identifiers used with service provider | Operator’s or MS-ISDN | Identity Provider’s Identifier (e.g. service provider or MNO such as IMSI) | Unique identity that is associated with Service Provider | Provider’s Identifier (e.g. service provider or MNO) format) | MNO provisioned ID | Identity Provider’s Identifier (e.g. service provider or MNO)
Specialized UICC, Smartcard required? | Yes (modified UICC) (not every UICC supports remote App download) | Yes - Many phones still do not support GBA at this point | Yes (smart card) | No | Yes - Many phones still do not support GBA at this point | No

## Slide 5: Comparison 2/3
Property | GSMA MobileConnect | 3GPP SSO | FIDO | Mobile Profile OpenID Connect | GBA | Proposed
Operator / NW involvement | Use of operator controlled credentials | Use of operator controlled credentials | Bit pipe only | Bit pipe only | Use of operator controlled credentials | Use of operator controlled credentials
User’s input | PIN. Password not required (though Apps may) | App password | App password | App password + OTP input received from operator | None | App password
What to standardize – and where | New UICC New identity assertion interface between MNO and service provider | As in SA3 TR (study phase) | As proposed by FIDO |  |  | An OMA multi-factor API to use & bind MNO credential as one factor
API to enable integration of MNO credentials into multi-factor authentication? | No | No | No | No | No | Yes subject of proposal

## Slide 6: Comparison 3/3
Property | GSMA MobileConnect | 3GPP SSO | FIDO | Mobile Profile OpenID Connect | GBA | Proposed
Strength of Authentication | Weakened by use of weak PIN | As strong as UICC | Depends on local FIDO client security | Simply confirms that someone is logged on device | As strong as UICC | Smart card security bound to App provider credentials
Binding between authentication factors | Not applicable | MNO credential bound to App credentials | No | Not applicable | Not Applicable | MNO credential bound to App credentials
Separation of credentials used for unlocking smart card | Single PIN for all Apps | Single PW for all Apps to run UICC Auth | Separate credential for each application service provider | Not applicable | Not Applicable | Not Applicable

## Slide 7: Summary of Analysis
Five user authentication techniques have been examined for this discussion paper
Of those:
  Three authenticate the user to UICC or smart card
  Two rely on GBA which seems to suffer acceptance issues
  Two either require extra user load or practically use the same (possibly weak) credentials for all applications
  One doesn’t even authenticate a specific user
  None (to the best of our knowledge ) enables an OTT identity provider or an application service provider to request an operator to provide a UICC based authentication factor for a multi-factor authentication
We propose to study the proposed approach for possible standardization by OMA. The study should produce an RD and an AD.

## Slide 8: References
3GPP SSO in 33.894 and 33.924
GBA in 33.934
OpenID Connect in http://openid.net/wg/mobile/charter/ and http://openid.bitbucket.org/Mobile_Profile_initial_draft_016.pdf and http://www.gsma.com/oneapi/wp-content/uploads/2014/06/GSMA-ID-MAE-Developer-Day.pdf
FIDO in https://fidoalliance.org/specifications/download/
GSMA e.g. in http://www.gsma.com/personaldata/mobile-connect-animation