## Slide 1: Proposal for MBMS Group Service Announcement in LwM2M 1.1
Submitted To: DM
Date: 19 May2017
Availability: Public OMA Confidential
Contact: Chris Lowe，chris.lowe@neul.com
Ada, xiaoyang.xiao@Huawei.com
Echo, echo.xubei@huawei.com
Source: Huawei
X
USE OF THIS DOCUMENT BY NON-OMA MEMBERS IS SUBJECT TO ALL OF THE TERMS AND CONDITIONS OF THE USE AGREEMENT (located at http://www.openmobilealliance.org/UseAgreement.html) AND IF YOU HAVE NOT AGREED TO THE TERMS OF THE USE AGREEMENT, YOU DO NOT HAVE THE RIGHT TO USE, COPY OR DISTRIBUTE THIS DOCUMENT.
THIS DOCUMENT IS PROVIDED ON AN "AS IS" "AS AVAILABLE" AND "WITH ALL FAULTS" BASIS.
Intellectual Property Rights
Members and their Affiliates (collectively, "Members") agree to use their reasonable endeavours to inform timely the Open Mobile Alliance of Essential IPR as they become aware that the Essential IPR is related to the prepared or published Specification. This obligation does not imply an obligation on Members to conduct IPR searches. This duty is contained in the Open Mobile Alliance application form to which each Member's attention is drawn. Members shall submit to the General Manager of Operations of OMA the IPR Statement and the IPR Licensing Declaration. These forms are available from OMA or online at the OMA website at www.openmobilealliance.org.

## Slide 2: Rational of MBMS group Service Announcement
Rationale :
  When massive NB-IoT devices upgrade firmware, because the NB-IoT network downlink bandwidth is < 200 kbit/s, it will take a long time to download the firmware package and the power consumption is very high during the downloading. It’s a big challenge to deploy NB-IoT.
  3GPP MBMS Group message delivery is intended to efficiently distribute the same content to the members of a group that are located in a particular geographical area. It can solve the problem of NB-IoT device upgrade.
  The security between LwM2M client and server can be ensured by 3GPP.
  LwM2M 1.1 has support ed 3GPP CIoT(NB-IoT and LTE CAT-M) and firmware upgrading enhancement
Proposal
LwM2M 1.1 supports to 3GPP MBMS mechanism to finish NB-IoT device upgrade.
  Defined a MBMS Group Service Announcement object to store the mapping between TMGI, the IP multicast address/port, local member object/resource and the fanOutPoint (virtual) of the multicast request, and about the schedule, ResponseTimeWindow.

## Slide 3: New Object Definition
Proposed Object & Description:
Name | Object ID | Instances | Mandatory | Object URN
MBMS Service Management | 50? | Multiple | Optional | urn:oma:lwm2m:x:50？
ID | Name | Operations | Instances | Mandatory | Type | Description
0 | TMGI | RW | Single | Mandatory | String | Temporary Mobile Group Identity, 1*15DIGIT, identifies a group bearer service
1 | IP Source address | RW | Single | Mandatory | string | The source address of the content delivered over the group bearer service
2 | IP Multicast address | RW | Single | Mandatory | string | IP Multicast address of group bearer service
3 | Destination port | RW | Single | Mandatory | Integer | Multicast destination UDP ports used on the group bearer service
4 | Schedule | RW | Multiple | Mandatory | Time?? | Every resource instance includes a pair of StartTime-Stop Time which is the time interval to receive the MBMS message.
5 | ResponseTimeWindow | RW | Single | Mandatory | Integer | A random time window, Unit :Second; the client response the MBMS after this random time to avoid the network congestion.
6 | Disable | E | Single | Optional |  | Disable the group bearer service
7 | fanOutPoint | RWE | Single | Mandatory | virtual | When this resource is accessed, the client shall replace the requested path with LocalMemPath, and then enhance the request
8 | LocalMemPath | RW | multiple | optional | string | path of the member on this client：objectID/objectInstanceID[/resourceID]

## Slide 4: Use Case 1
Illustration:
  Example Use Case 1: LwM2M Server creates MBMS group object to members by Unicast to associated with MBMS TMGI and IP multicast address and to provide a fanOutPoint to LwM2M server
LwM2M Sever
3GPP Network
LwM2M Client
(UE1)
1 TMGI Allocation
LwM2M Client
(UE2)
2 Create MBMS Service Management object by Unicast
2 Create MBMS Service Management object by Unicast
Req: POST coap://50/
Payload:
{“bn”:”/50/0”,
“e”:[
{“n”:”0”,”12345”},
{“n”:”1”,”sv”: ”10.123.45.6”},// LwM2M server address
{“n”:”2”,”sv”: ”224.0.1.3:24”},//
{“n”:”3”,”sv”:80},
{“n”:”3”,”sv”:80},
{“n”:”3”,”sv”: 1498233600 - 1498244400},// 2017/6/24 00:00:00 - 2017/6/24 03:00:00
{“n”:”5”,”sv”:300},
{“n”:”7”,},
{“n”:”8”,”sv”:/5/0/0},//for UE1, /5/1/0 for UE2
} Note: the object instance id is assigned by LwM2M server.
3 Observe State (put, 5/0/3) by Unicast
3 Observe State (put, 5/0/3) by Unicast

## Slide 5: Use Case 2
Illustration:
  Example Use Case 1: LwM2M Server send firmware package to all members via 3GPP MBMS
  After LwM2M client receiving the multicast POST request, each LwM2M client finds the localMemPath according the /50/0/0 and replaces the /50/0/0 with the localMemPath (e.g. /5/0/0), then update the value (of /5/0/0) and returns to LwM2M Server
  LwM2M client send the Notify to Server when event triggers
LwM2M Sever
3GPP Network
LwM2M Client
(UE1)
1 TMGI Active Bearer
LwM2M Client
(UE2)
2 Write firmware package by MBMS
  Req: POST coap://50/0/0
  HOST URI : 224.0.1.3:24;
3 Notify status 2
3 Notify status 2

## Slide 6: The Impact
Impact :
  LwM2M server needs to send the MBMS related information(TMGI, StartTime,etc) to the client
  One New object --- MBMS Service Management
  One new resource type – virtual
  A mechanism is needed to make sure that LwM2M server can assign the same object instance id of MBMS Service Management object on the different devices/clients,
  Both LwM2M server or LwM2M client need to support the MBMS as specified in [3GPP 23.682]
Supporters : HUAWEI

## Slide 7
Refer 1:3GPP TS29.682 Group Message Delivery
We can assume SCS/AS as LwM2M Server
Step 5/12:Application level interactions may be applied for the devices of specific group to retrieve the related MBMS service information, e.g. TMGI, start time. Application level interactions between the UE and the SCS/AS are out of scope of 3GPP specification.

## Slide 8
Refer 2:3GPP TS29.468
Figure 7.1‑1 depicts the MB2‑U protocol stack without security protocols. The stack shall include:
1)User plane data, for instance an IP layer and UDP layer. The user plane data are transparently transported between the GCS AS and the UE. The BM‑SC shall forward these protocol layers transparently.
-2)UDP according to IETF RFC 768 [12]. UDP shall be terminated at the GCS AS and BM‑SC.
-3)IP transported by lower layers L1 and L2. These layers shall be terminated at the GCS AS and BM‑SC.
UDP shall be terminated at the GCS AS and BM‑SC.
IP transported by lower layers L1 and L2. These layers shall be terminated at the GCS AS and BM‑SC.
User plane data, for instance an IP layer and UDP layer. The user plane data are transparently transported between the GCS AS and the UE. The BM‑SC shall forward these protocol layers transparently.
7 MB2‑U Protocol
7.1 Protocol Stack

## Slide 9: User Data Plane Structure For LwM2M
UDP
IP
HTTP
LwM2M
COAP
UDP
IP
TCP
IP
LwM2M Server
SCEF
LwM2M
COAP
UDP
IP
3GPP TS36.300
UE
LwM2M Server
TCP
HTTP
eNodeB/BM-SC
LwM2M interface
POST, /50/0(fanOutPoint)
Destination IP: multicast Address
Multicast
unicast
Multicast
unicast
T8
GMD
GMD
MB2-U
LET-Uu