## Slide 1: LwM2M v1.1
Lightweight Machine to Machine
Open Mobile Alliance

## Slide 2: LightweightM2M (LwM2M) is a Device Management Protocol
O-ID
R-ID
R-ID
5701
…
Switch
Drvr
Temp
Drvr
H/W Sensors
Driver
Sensors
Constrained Device
/
Client LwM2M
Remote
Server
LwM2M
Sensor(s)
Object/Resource
Data Model
Temp (3303)
Relay (3342)
*Bootstrapping | Device Configuration | Firmware Update | Fault Management |Configuration & Control |Reporting
One object for each sensor
*Device Management Functions
(3303)
10KB RAM, 100KB Flash, 40 MHZ

## Slide 3: LwM2M Protocol stack
Objects
Application
IPSO WG
Data Model
Messaging
Resource Model
Device Management
Onboarding
CRUDN
Security
Security
Authentication

## Slide 4: Data Model

## Slide 5: M2M in the Telecom Network: The target for LwM2M Devices
Public Safety
Automotive
Industrial Automation
Energy
Smart City
Health Care
M2M Service Layer
M2M Devices
Telecom Network
Services
Source: Open Mobile Alliance

## Slide 6: Introduction
LwM2M is recommended for Device Management and Service Enablement because its benefits include:
Increased bandwidth efficiency based on COAP bandwidth optimization
Transport-agnostic design that supports UDP, TCP, SMS
Developer toolkit for application development
DTLS-based security based on CoAP (IETF)
Low power client foot print designed for battery constrained devices
End to end security using IETF OSCORE
Device Management & Service Enablement
Application
S e c u r e & B W e f f i c i e n t
LwM2M server
LwM2M client
Objects
M2M device
Objects
Stack
Efficient payload
CoAP protocol
DTLS security
TCP or UDP or SMS bearer
NIDD
Interfaces
Bootstrapping
Registration
Object/resource access
Reporting
Billing and Usage
Managed remote asset(s)
Notes: This slide is a pure styling rework based on the look of the other slides

## Slide 7: Strengths of LWM2M
LwM2M can be used for both data plane (data reporting and devices actuations) and device management.
LwM2M is a standard defined by OMA
Suitable for both fixed and mobile devices
Appropriate for both data plane and device management
Designed for constrained devices (e.g < 20 kB RAM)
Suitable for low powered battery devices because of its low client footprint
Minimizes bandwidth due to optimized bandwidth consumption by utilizing COAP (COAP is a simplified HTTP; COAP header = 4bytes)
Simple, stateless protocol
Crosses FW and NAT systems thanks to support of COAP/UDP and COAP/TCP
Offers security by design; COAP over UDP or TCP relies on DTLS or TLS respectively
Provides opportunities for e2e security

## Slide 8: LWM2M: Core functionalities
LWM2M
Boot-strapping
Device Config.
Firmware Update
Diagnostics
Connection Mgmt.
Control
Data
Reporting
Lock & Wipe

## Slide 9: Bootstrap Interface

## Slide 10: Device Configuration

## Slide 11: Firmware Update

## Slide 12
Power sources and LwM2M Device settings
Battery level of the LwM2M Device
Memory status of the LwM2M Device
Supported binding modes of the LwM2M Device
Version of hardware/software of the LwM2M Device
Capabilities of the LwM2M Device
Diagnostics

## Slide 13
Mapping of necessary Cellular and Wi-Fi technologies
Managing basic parameters needed for the technologies to function e.g. APN, WEP keys etc.
Adding relevant parameters for bearer selection for cellular connectivity
Security is covered by DTLS
Connection Management

## Slide 14
Ability to setup access control on Objects for various LwM2M servers
Wake up the LwM2M Device using SMS
Reboot the LwM2M Device
Disable the LwM2M Device for a specified time
Ask the LwM2M Device to perform registration
Control

## Slide 15: Data Reporting

## Slide 16: Lock & Wipe

## Slide 17
Types of credential procedures supported
Certificates
Pre-shared key
Public Raw Key
PKI deployments
Security paths
DTLS
SMS
DTLS over SMS
OSCORE
LwM2M Security abilities
Initial keys can be replaced during bootstrap procedure
Multiple servers could be added with different credentials
Provide security in every path
LwM2M Security

## Slide 18
LwM2M security – continued
Security Keys
Bootstrap Server
LwM2M Device
LwM2M Server1
Factory
Provisioned
Provisioning after
First contact
First
Contact
Pre-
provisioned
LwM2M Server2
Using Provisioned
Credential 1
Using Provisioned
Credential 2

## Slide 19
Simple resource model with the core set of objects and resources defined in the specification. The full list of registered objects can be found in the LwM2M registry.
Operations for creation, update, deletion, and retrieval of resources.
Asynchronous notifications of resource changes.
Support for several serialization formats, namely TLV, JSON, Plain Text and binary data formats and the core set of LightweightM2M Objects.
UDP and SMS transport support.
Communication security based on the DTLS protocol supporting different types of credentials.
LwM2M v1.0 features

## Slide 20
Queue Mode offers functionality for a LwM2M Client to inform the LwM2M Server that it may be disconnected for an extended period of time and also when it becomes reachable again.
Support for use of multiple LwM2M Servers.
Provisioning of security credentials and access control lists by a dedicated LwM2M bootstrap-server.
LwM2M v1.0 features continued

## Slide 21
Improved support for Public Key Infrastructure (PKI) deployments.
Introduction of enhanced registration sequence mechanisms by the LwM2M Client to LwM2M Server(s).
Support for LwM2M over TCP/TLS to better support firewall and NAT traversal.
Support for application layer security for LwM2M based on OSCORE.
Better support of LwM2M over Low Power WANs, including 3GPP CIoT & LoRaWAN.
Extended LwM2M commands to enable Resource Instance level access.
Performance improvement for retrieving and updating Resources of multiple objects.
Support for JSON using SenML with CBOR serialization for compressed payload with highly efficient transmission.
LwM2M v1.1 features

## Slide 22
Enhanced Registration Sequence

## Slide 23
Security & additions to v1.1

## Slide 24
Support of LPWAN – 3GPP CIoT

## Slide 25
Support of LPWAN – LoRaWAN

## Slide 26: Objects from OMASpecWorks
LwM2M Security
LwM2M Server
LwM2M Access Control
Device
Connectivity Monitoring
Firmware Update
Location
Connectivity Statistics
Cellular Connectivity
APN Connection Profile
WLAN Connectivity
Bearer Selection
Communication Characteristics
Non-Access Stratum (NAS) Configuration
LwM2M OSCORE
Lock and Wipe
DevCapMgmt
Portfolio
LwM2M Software Management
LwM2M Software Component
BinaryAppDataContainer
Event Log

## Slide 27: Objects registered OMASpecWorks
Power Control
Light Control
Accelerometer
Magnetometer
Barometer
Altitude
Load
Pressure
Loudness
Gyrometer
Addressable Text Display
Multiple Axis Joystick
Multi-state selector
Dimmer
powerupLog
radioLinkFailureEvent
cellBlacklistEvent
NeighborCellMeasurements
ServingCellMeasurement
PagingDRX
txPowerBackOffEvent
SipRegistrationEvent
sipSubscriptionEvent
VolteCallEvent
volteCallStateChangeEvent
Refer LwM2M registry for full list - http://www.openmobilealliance.org/wp/OMNA/LwM2M/LwM2MRegistry.html

## Slide 28
Comparing Equivalent Standards in mobile space
Areas | OMA-DM 1.x | LwM2M v1.1
Device Management | Established and stable | Growing
Firmware Updates | Partial Standardized | Partial Standardized and expanding
Scalability | Targeting bigger devices | Wide Range feasible
Use in Constrained Devices | No | Yes
IoT enablement | Bigger devices feasible but data model needs evolution | Data Model evolved for IoT enablement and is expanding
Active Standardization members | None | Stable with additional standards working on top
Service Enablement | Limited to Telecom Features | Expanding into other IoT/verticals
Service level standardization | - NA - | IRTF T2TRG actively collaborating to expand semantic interoperability on top of LwM2M (OCF, W3C WoT, Fairhair Alliance )
Supporting Standardization Groups | GSMA, 3GPP | GSMA, IPSO (assimilated into OMA), IETF, IRTF, OpenAIS, oneM2M and expanding..

## Slide 29: Status with Industry & market
ARM
AVSystem
Cumulocity
Ericsson
Friendly Technologies
Gemalto
Huawei
IOTECC
IoTerop
Itron
Nokia
Orange
Qualcomm
Sierra Wireless
Smith Micro
Telit
u-blox
Note: A large number of companies around the world are working on LwM2M implementations including many small and medium sized companies.

## Slide 30
235 million of LwM2M-enabled devices are expected to be deployed by 2022
  “IDATE explored the market opportunities over four markets including automotive, utilities, building automation and logistics. The total installed base of LwM2M-enabled devices will reach over 235 million units in 2022, from less than 0.5 million units in 2015,” said Samuel Ropert, Head of IoT Practice at IDATE Digiworld. “This represents a CAGR of 154% in the 2015-2022 period.” https://www.omaspecworks.org/oma-lightweightm2m-v1-0-approved-by-board-of-directors/
LwM2M Forecast